MULTNOMAH COUNTY, OREGON

ADMINISTRATIVE PROCEDURE		RSK-16

SUBJECT:				Lockout/Tagout (Control of Hazardous Energy)

PURPOSE:				The purpose of this administrative procedure is to ensure that before any employee performs any servicing or maintenance on a machine or piece of equipment, the machine or equipment is isolated and rendered inoperative. This procedure for control of lockout/tagout devices covers the servicing and maintenance of machines or equipment in which the unexpected energizing or start-up of the machine or equipment, or the release of stored energy, could cause injury to employees.

ORGANIZATION

RESPONSIBLE:			Department of Business and Community Services, Business Services, Human Resources – Safety, Health and Workers’ Compensation

DATE:					Diane M. Linn			10/2004

ORGANIZATIONS

AFFECTED:				All Departments/Offices

LEGAL CITATION/

REFERENCE:			OAR 437-2/J-1910.147 “The Control of Hazardous Energy (Lockout/Tagout).”

MCC 7.100 to 7.202.

I.	PROCEDURE DESCRIPTION

A.	General

1.	This procedure is applicable to all Departments/Offices.

2.	This procedure is intended to meet the requirements for a written 				lockout/tagout program as set forth in Oregon Occupational Safety 				and Health Division (OR-OSHA) regulation 437-2/J-1910.147.

3.	This procedure covers equipment and machines at all Multnomah 				County sites, or equipment under the control of County employees 				regardless of location.  Note that this program does not apply to cord 				and plug equipment that can be unplugged and is under complete 				control of the person doing the work.

4.	The items contained in this procedure are mandatory and are a 				condition of employment for all individuals.

II.	DEFINITIONS

A.	Affected Employee:  An employee whose job requires them to operate 			or use a machine or piece of equipment on which servicing or 					maintenance is being performed under lockout or tagout, or whose 				job requires them to work in the area.

B.	Authorized Employee: An employee who locks or implements a tagout 			system on machines or pieces of equipment and has been trained to do so.

C.	Energy Isolating Device: A mechanical device that physically prevents the 		transmission or release of energy.

D.	Energy Source: Any source of electrical, mechanical, hydraulic, pneumatic, 		chemical, thermal, or other energy.

E.	Lockout:  Placement of a lockout device on an energy isolating device 			ensuring that the energy isolating device and equipment being controlled 			cannot be operated until the lockout device is removed.

F.	Lockout Device:  A device, such as a lock, placed on an energy-isolating 			device to prevent the energizing of a machine or equipment.

G.	Tagout: Placement of a tagout device on an energy isolating device 				indicating that the energy isolating device and equipment being controlled 			may not be operated until the tagout device is removed.

H.	Tagout Device:  A prominent warning device that can be securely fastened 		to an energy isolating device to indicate that the energy isolating device and 		equipment being controlled may not be operated until the tagout device is 			removed.

III.	BASIC PROGRAM REQUIREMENTS

A.	Authorized Employees

Only Authorized Employees may apply and remove lockout/tagout devices.  		Each Department will designate and maintain a list of Authorized 				Employees.

B.	Contractors and other Non-Multnomah County Personnel

Any non-Multnomah County personnel working on County sites, including 			private contractors, utility workers, volunteers, or other public employees, 			must be notified of the Multnomah County lockout/tagout program when 			their responsibilities require working on any type of energized equipment 			that may affect Multnomah County employees.  A copy of this Procedure 			will be given to, or discussed with, the contractor and a mutually agreed 			upon procedure will be established to fully protect the contractor and 				Multnomah County employees.

C.	Lockout and Tagout Devices

These devices must meet the following criteria:

- They must be singularly identified and will be the only devices used for controlling energy and not be used for other purposes;

- They must be standardized in at least one of the following criteria:  color, shape, or size.  Additionally, when tagout devices are used they will be standardized with respect to print and format.  Attachment D of this policy gives an example of acceptable tags;

- Lockout and tagout devices will indicate the identity of the employee applying the device;

- Tagout devices will warn against specific hazardous conditions if the machine or piece of equipment is energized, and will include a legend such as the following:  “Do Not Start,” “Do Not Open,” “Do Not Close,” “Do Not Energize,” “Do Not Operate.”

D.	Lockout/Tagout Procedures

If an energy-isolating device is capable of being locked out, then lockout 			must be used.  If an energy-isolating device is not capable of being locked 			out, a tagout device must be used.  Per OR-OSHA regulations, all new 			equipment, or equipment subject to major repair or modification, must have 			an energy-isolating device capable of accepting a lockout device.

- Before a machine or piece of equipment is turned off, the authorized employee will know the type and magnitude of the energy, the hazards of the energy to be controlled, and the method or means to control the energy.  More than one energy source may be involved;

- All affected employees will be notified that a lockout or tagout device is going to be utilized and the reason for it;

- An orderly shutdown must be utilized to avoid any additional hazards to employees.  Shut down the machine or piece of equipment using the normal shutdown procedures;

- Lockout or tagout devices will be affixed to each energy-isolating device by the Authorized Employee. Lockout devices will be affixed in a manner that will hold the energy-isolating device in a safe or off position;

- Following the application of lockout or tagout devices, all potentially hazardous stored or residual energy will be relieved, disconnected, restrained, or otherwise rendered safe;

- Prior to starting work on machines or equipment which have been locked or tagged out, the Authorized Employee must verify that isolation and de-energizing of the machine or equipment has been accomplished. This is accomplished by attempting to start the machine or piece of equipment;

- After completing step 6, return operating controls to the neutral or off position.

E.	Equipment Testing While Under Lockout/Tagout

In some instances it may be necessary to operate equipment or machines 			during maintenance or servicing.  If so, the following steps must be taken to 			protect personnel:

- Clear the equipment or machine of all tools and materials that are non-essential items;

2.	Make sure that all personnel are clear of the equipment or machine and notify them that the machine will be energized;

- 3.  The Authorized Employee will remove the lockout or tagout device;

- 4. Energize the machine or equipment and proceed with testing or positioning;

- 5. After testing or positioning, de-energize the equipment or machine, complete all shutdown procedures, and reapply lockout or tagout devices before continuing with further maintenance or servicing.

F.	Work on Energized Equipment or Systems

In some cases work must be done on a piece of equipment or system while 		it remains energized.  An example of this is an electrical system that cannot 			be taken off-line while work is being done on it.  In these cases, procedures 			and practices must be in place to ensure the safety of personnel working on 		or near the energized equipment or system.

Procedures and practices which may be used as appropriate to ensure 			personnel safety include, but are not limited to:

- Ensuring only properly trained and knowledgeable personnel work on the energized equipment/system;

- Utilizing appropriate protective equipment (e.g. insulated tools and PPE) when working on the energized equipment/system; and

- Performing work on the energized equipment/system when the least number of non-essential personnel are around (evenings, weekends).

G.	Release from Lockout/Tagout

Before lockout or tagout devices are removed and energy is restored, the 			Authorized Employee must ensure that nonessential items have been 			removed and that machine or equipment components are intact.  In 				addition, the Authorized Employee must ensure all other employees have 			been safely positioned or removed from the area.

Each lockout or tagout device will only be removed by the employee who 			applied the device.  If that employee is not available, the device can be 			removed providing the following conditions are met:

a.	It has been verified that the employee is not at the site;

b.	A reasonable effort has been made to contact the employee to 	inform them about the removal;

c.	The employee is informed about the device removal before that 	employee resumes work at the site;

d.	Standard procedures for removing a lockout/tagout device are 		followed;

e.	Only the supervisor of the employee who attached the device 	may remove it;

f.      Notice of device removal will be posted at the site for a minimum          of one shift or until the authorized employee returns to the site;

g.	If a contractor attached the device, only the contractor’s 	supervisor may remove the device.  If the contractor’s supervisor 	cannot be located, the Multnomah County site supervisor can 	remove the device following steps “a” through “f;”

h.	Attachment A “Removal of a Lockout or Tagout Device by a 	Supervisor” must be completed each time a supervisor removes 	an employee’s or contractor’s device.

After the lockout or tagout devices have been removed, operate the energy isolating device(s) to restore the equipment or machine to its normal operational condition.

H.	Procedures Involving More Than One Person

OR-OSHA regulations allow for “group lockout or tagout.”  This system of 			employee protection may be used when a large group of employees is 			working on a piece of equipment.

Ideally, group lockout/tagout should not be used.  Each employee working 			on a piece of equipment should place their own locks or tags on the energy-			isolating device.  There are devices available which will accommodate 			multiple locks or tags.

If group lockout/tagout is necessary, the lockout/tagout procedures 				described above should be used.  In addition to these procedures, the 			following must also be done when using a group lockout/tagout:

- Primary responsibility will be vest in one Authorized Employee for a set number of employees in the group lockout/tagout;

- This Authorized Employee must verify that all employees working under them in the group lockout/tagout remain protected against machine startup;

- If multiple entities (e.g. departments, contractors) are covered under the group lockout/tagout, one Authorized Employee will be responsible for coordinating the lockout/tagout activity for all entities to assure all employees are protected; and

- Each Authorized Employee in the group lockout/tagout will place a personal lock or tag to the group lockout device when they begin work, and remove it when they are finished working on the equipment.

I.	Special Rules Regarding Tags

Tagout devices may only be used when the energy-isolating device is not 			lockable.  It is very important for employees to understand the differences 			between locks and tags.  The use of tags may give a false sense of 				security.

- Tags are essentially a warning device only.  They do not provide any type of physical restraint or energy isolation;

- When tags are applied they must be signed and dated by the employee applying the tag and may not be removed by anyone except that employee;

- Tags must never be bypassed, ignored, or otherwise defeated;

- Tags must be legible and understandable by all employees and contractors who work in the area where the tags are used;

- Tags must be uniform in color, size, and design so as to be easily recognized.  Attachment D to this policy gives an example of acceptable tags;

- Tags and their means of attachment will be durable and made of a material able to withstand the environmental conditions encountered in the workplace;

- Tags must be securely attached to energy isolating devices so that they cannot be inadvertently detached during use;

- Tag attachment devices must not be reusable.  Nylon wire straps or other similar type devices will be used.

J.	Training

All employees impacted by lockout/tagout procedures will receive training 			to ensure that the purpose and content of this program are understood.  			Training for all employees will include:

- Recognition of applicable energy sources, the type and magnitude of the energy available in the workplace, and the methods and means necessary for energy isolation and control;

- The purpose and use of the lockout and tagout procedures;

- The prohibition of attempts to restart or reenergize machines or equipment which are locked or tagged out;

- When tagouts are used instead of lockouts, the following limitations of tags:

- Tags are warnings and do not physically lock energy isolating devices, thus they may evoke a false sense of security.  The meaning of the tag must be understood;

- Tags can only be removed by the person who applied it, and that the tag is never to be ignored or bypassed;

- Tags must be legible and understandable by all employees using them as well as affected employees.

- Training will be provided upon initial assignment to the site.  Retraining will be provided whenever there is a change in job assignments, a change in machines or equipment that present a new hazard, or when there is a change in energy control procedures.  Retraining will also be conducted as part of the periodic assessment, and whenever site management has reason to believe that there are deviations from the established procedures.

K.	Equipment Specific Procedures

Attachment B “Equipment Specific Lockout/Tagout Procedures” must be 			completed for each individual machine or piece of equipment that must be 		locked or tagged out if the equipment or machine:

- 1.   Has the potential for stored or residual energy after shutdown;

2.   Has the potential for reaccumulation of stored energy after shutdown;

- 3.   Can be energized from more than one source;

- 4.   Cannot be completely deenergized and deactivated by one energy source;

- 5.   Needs more than one lockout device to lockout the equipment;

- 6.   Has a lockout device that is not under the exclusive control of the authorized employee performing the maintenance;

- 7.   Requires maintenance activities that may create hazards for other employees, even though the equipment is locked out.

The procedure can be maintained in any other written format as long as 			the information in Attachment B is covered.

L.	Periodic Assessments

Periodic assessments will be conducted at least annually by site 				supervisors or their designate.  The employees using lockouts or tagouts 			will be interviewed during the assessments concerning their 					responsibilities.  Assessment records will include:

- The identity of the machine or piece of equipment on which the lockout or tagout procedures were utilized;

- The date of the assessment;

- Names of employees who were included in the assessment;

- Person performing the assessment.

Attachment C “Periodic Lockout/Tagout Assessment Form” will be used to 		document the assessments.

IV.	RESPONSIBILITIES

A.	Safety, Health, and Workers’ Compensation Section has the following basic responsibilities:

- Assist sites in developing specific lockout/tagout procedures;

- Periodically review this Administrative Procedure to ensure it is up to date;

- Assist sites in lockout/tagout training.

- Assist sites in equipment specific procedure documentation.

B.	Departments/Divisions

Departments/Divisions have the following basic responsibilities:

- Implementing this Administrative Procedure at their facilities and/or for their employees;

- Establishing equipment specific procedures where applicable;

- Ensuring the appropriate Department/Division personnel are trained on the elements of the lockout/tagout program;

- Interfacing with contractors regarding lockout/tagout procedures;

- Ensuring procedures and practices are in place to protect personnel if they have to work on energized equipment or systems.

C.	Employees

Employees have the following basic responsibilities:

- Following all rules and directions regarding lockout/tagout procedures;

- Not attempting to operate equipment that is locked or tagged out.

III.    IMPLEMENTATION AND INTERPRETATION
Any questions relative to the intent or application of this procedure should be directed to the Safety and Health Program Manager who is responsible for interpreting and implementing this procedure.

(Attachments are on the following pages)

ATTACHMENT A

REMOVAL OF A LOCKOUT OR TAGOUT DEVICE BY A SUPERVISOR

POST UNTIL (Date):____________________________________

(At least one shift, or until the affected individual returns to work, whichever is longer.)

DATE

SITE

SUPERVISOR WHO REMOVED DEVICE

EMPLOYEE WHOSE DEVICE WAS REMOVED

SUPERVISOR ATTEMPTED TO CONTACT EMPLOYEE (date, time method)_________

OTHER EMPLOYEES INVOLVED

EQUIPMENT INVOLVED

FULLY DESCRIBE THE CIRCUMSTANCES THAT NECESSITATED REMOVAL OF THE LOCKOUT OR TAGOUT DEVICE

SUPERVISOR SIGNITURE

EMPLOYEE acknowledgement of personal lock removal:		Date:

ATTACHMENT B

EQUIPMENT SPECIFIC LOCKOUT/TAGOUT PROCEDURE

Machine or Equipment:___________________________		Names of Authorized Employees:

___________________________

___________________________

___________________________

| Type of Energy (e.g. Electric, Steam, Air) | Magnitude of Energy (e.g. Voltage, Temp., Pressure) | Type & Location of Energy Isolating Device(s) (e.g. Breaker, Valve) | Method(s) of Isolation (e.g. Lock on breaker, Chain and lock valve) | Steps Taken to Verify Isolation |
| --- | --- | --- | --- | --- |

Procedure Approved by:								Date:

ATTACHMENT C

PERIODIC LOCKOUT/TAGOUT ASSESSMENT FORM

ASSESSOR:

DATE OF ASSESSMENT:

EMPLOYEE(S) BEING ASSESSED:

EQUIPMENT ASSESSMENT PERFORMED ON:

Was notification of affected employees completed prior to beginning lockout/tagout?

YES						NO

Were all sources of energy identified, controlled or relieved?  Was this verified by activating equipment controls?

YES						NO

Were correct locks and/or tags used?  If locks, were these specifically assigned to the employee?

YES						NO

Does the lockout or tagout device clearly identify who applied the device?

YES						NO

If testing of the equipment was required, did the employee effectively re-energize, de-energize, and return the equipment to the correct locked out or tagged out condition?

YES						NO

Did the employee correctly release the equipment from lockout or tagout?

YES						NO

YES	NO	All tools removed from equipment, and all equipment components 			intact?

YES	NO	Affected employees warned of equipment start-up?

YES	NO	Verified equipment operating controls in off or neutral position?

YES	NO	Removed the lockout/tagout device and energized equipment?

YES	NO	Notified affected employees of equipment status?

NOTES/COMMENTS/RECOMMENDATIONS:

ATTACHMENT D

EXAMPLE OF ACCEPTABLE TAGOUT DEVICES

The following tags, or substantially similar ones, must be used when locking and/or tagging out equipment.  These tags are available from safety supply vendors.